## Slide 1
pIC_MVMp
BamHI
Poly(dG)
NS1/2
VP1/2
AmpR

## Slide 2
Plasmid | pIC_MVMp*
bp | 8992
MW | 2’782’973 Da
OD 280 (1:10 diluted) | 1.694
OD 260 (1:10 diluted) | 3.234
OD 260/280 | 1.91
Concentrtaion | 1.617 μg/μL
Copies / μL | 3.499 × 1011
Date of preparation | 05.05.2015
Operator | R. Wolfisberg
MVM infectious clone and
standard for qPCR
Laboratory: Prof C Kempf
Dept Chemistry and Biochemistry
Preparation:
Briefly, cells (E. coli XL-1 blue) were transformed with the plasmid pIC_MVMp, and cultured overnight. Subsequently the plasmid was isolated using Qiagen Plasmid Midi kit (Cat. # 12145). The DNA was resuspended in AE buffer (Qiagen Dneasy Blood & Tissue kit; Cat # 69506). DNA concentration (and purity) in the extract was measured by determination of the absorption at OD260/280.
*The plasmid was obtained from Prof J.M. Almendral, Centro de Biología Molecular "Severo Ochoa“; Nicolás Cabrera 1 Campus de la Universidad Autónoma de Madrid. Cantoblanco. 28049 Madrid. Spain. MVM coding region confirmed by sequencing.

## Slide 3
Sequence plasmid pIC_MVMp (MVM sequence)
ttcttgaagacgaaagggcctcgtgatacgcctatttttataggttaatgtcatgataataatggtttcttagacgtcaggtggcacttttcggggaaatgtgcgcggaacccctatttgtttatttttctaaatacattcaaatatgtatccgctcatgagacaataaccctgataaatgcttcaataatattgaaaaaggaagagtatgagtattcaacatttccgtgtcgcccttattcccttttttgcggcattttgccttcctgtttttgctcacccagaaacgctggtgaaagtaaaagatgctgaagatcagttgggtgcacgagtgggttacatcgaactggatctcaacagcggtaagatccttgagagttttcgccccgaagaacgttttccaatgatgagcacttttaaagttctgctatgtggcgcggtattatcccgtgttgacgccgggcaagagcaactcggtcgccgcatacactattctcagaatgacttggttgagtactcaccagtcacagaaaagcatcttacggatggcatgacagtaagagaattatgcagtgctgccataaccatgagtgataacactgcggccaacttacttctgacaacgatcggaggaccgaaggagctaaccgcttttttgcacaacatgggggatcatgtaactcgccttgatcgttgggaaccggagctgaatgaagccataccaaacgacgagcgtgacaccacgatgcctgcagcaatggcaacaacgttgcgcaaactattaactggcgaactacttactctagcttcccggcaacaattaatagactggatggaggcggataaagttgcaggaccacttctgcgctcggcccttccggctggctggtttattgctgataaatctggagccggtgagcgtgggtctcgcggtatcattgcagcactggggccagatggtaagccctcccgtatcgtagttatctacacgacggggagtcaggcaactatggatgaacgaaatagacagatcgctgagataggtgcctcactgattaagcattggtaactgtcagaccaagtttactcatatatactttagattgatttaaaacttcatttttaatttaaaaggatctaggtgaagatcctttttgataatctcatgaccaaaatcccttaacgtgagttttcgttccactgagcgtcagaccccgtagaaaagatcaaaggatcttcttgagatcctttttttctgcgcgtaatctgctgcttgcaaacaaaaaaaccaccgctaccagcggtggtttgtttgccggatcaagagctaccaactctttttccgaaggtaactggcttcagcagagcgcagataccaaatactgtccttctagtgtagccgtagttaggccaccacttcaagaactctgtagcaccgcctacatacctcgctctgctaatcctgttaccagtggctgctgccagtggcgataagtcgtgtcttaccgggttggactcaagacgatagttaccggataaggcgcagcggtcgggctgaacggggggttcgtgcacacagcccagcttggagcgaacgacctacaccgaactgagatacctacagcgtgagctatgagaaagcgccacgcttcccgaagggagaaaggcggacaggtatccggtaagcggcagggtcggaacaggagagcgcacgagggagcttccagggggaaacgcctggtatctttatagtcctgtcgggtttcgccacctctgacttgagcgtcgatttttgtgatgctcgtcaggggggcggagcctatggaaaaacgccagcaacgcggcctttttacggttcctggccttttgctggccttttgctcacatgttctttcctgcgttatcccctgattctgtggataaccgtattaccgcctttgagtgagctgataccgctcgccgcagccgaacgaccgagcgcagcgagtcagtgagcgaggaagcggaagagcgcctgatgcggtattttctccttacgcatctgtgcggtatttcacaccgcatatggtgcactctcagtacaatctgctctgatgccgcatagttaagccagtatacactccgctatcgctacgtgactgggtcatggctgcgccccgacacccgccaacacccgctgacgcgccctgacgggcttgtctgctcccggcatccgcttacagacaagctgtgaccgtctccgggagctgcatgtgtcagaggttttcaccgtcatcaccgaaacgcgcgaggcagctgcggtaaagctcatcagcgtggtcgtgaagcgattcacagatgtctgcctgttcatccgcgtccagctcgttgagtttctccagaagcgttaatgtctggcttctgataaagcgggccatgttaagggcggttttttcctgtttggtcacttgatgcctccgtgtaagggggaatttctgttcatgggggtaatgataccgatgaaacgagagaggatgctcacgatacgggttactgatgatgaacatgcccggttactggaacgttgtgagggtaaacaactggcggtatggatgcggcgggaccagagaaaaatcactcagggtcaatgccagcgcttcgttaatacagatgtaggtgttccacagggtagccagcagcatcctgcgatgcagatccggaacataatggtgcagggcgctgacttccgcgtttccagactttacgaaacacggaaaccgaagaccattcatgttgttgctcaggtcgcagacgttttgcagcagcagtcgcttcacgttcgctcgcgtatcggtgattcattctgctaaccagtaaggcaaccccgccagcctagccgggtcctcaacgacaggagcacgatcatgcgcacccgtggccaggacccaacgctgcccgagatgcgccgcgtgcggctgctggagatggcggacgcgatggatatgttctgccaagggttggtttgcgcattcacagttctccgcaagaattgattggctccaattcttggagtggtgaatccgttagcgaggtgccgccggcttccattcaggtcgaggtggcccggctccatgcaccgcgacgcaacgcggggaggcagacaaggtatagggcggcgcctacaatccatgccaacccgttccatgtgctcgccgaggcggcataaatcgccgtgacgatcagcggtccagtgatcgaagttaggctggtaagagccgcgagcgatccttgaagctgtccctgatggtcgtcatctacctgcctggacagcatggcctgcaacgcgggcatcccgatgccgccggaagcgagaagaatcataatggggaaggccatccagcctcgcgtcgcgaacgccagcaagacgtagcccagcgcgtcggccgccatgccggcgataatggcctgcttctcgccgaaacgtttggtggcgggaccagtgacgaaggcttgagcgagggcgtgcaagattccgaataccgcaagcgacaggccgatcatcgtcgcgctccagcgaaagcggtcctcgccgaaaatgacccagagcgctgccggcacctgtcctacgagttgcatgataaagaagacagtcataagtgcggcgacgatagtcatgccccgcgcccaccggaaggagctgactgggttgaaggctctcaagggcatcggtcgacgctctcccttatgcgactcctgcattaggaagcagcccagtagtaggttgaggccgttgagcaccgccgccgcaaggaatggtgcatgcaaggagatggcgcccaacagtcccccggccacggggcctgccaccatacccacgccgaaacaagcgctcatgagcccgaagtggcgagcccgatcttccccatcggtgatgtcggcgatataggcgccagcaaccgcacctgtggcgccggtgatgccggccacgatgcgtccggcgtagaggatccggggggggggggggttttagaactgaccaaccatgttcacgtaagtgacgtgatgacgcgcgctgcgcgcgctgccttcggcagtcacacgtcacttacgtttcacatggttggtcagttctaaaaatgataagcggttcagggagtttaaaccaaggcgcgaaaaggaagtgggcgtggtttaaagtatataagcaactactgaagtcagttacttatcttttctttcattctgtgagtcgagacgcacagaaagagagtaaccaactaaccatggctggaaatgcttactctgatgaagttttgggagcaaccaactggttaaaggaaaaaagtaaccaggaagtgttctcatttgtttttaaaaatgaaaatgttcaactgaatggaaaagatatcggatggaatagttacaaaaaagagctgcaggaggacgagctgaaatctttacaacgaggagcggaaactacttgggaccaaagcgaggacatggaatgggaaaccacagtggatgaaatgaccaaaaagcaagtattcatttttgattctttggttaaaaaatgtttatttgaagtgcttaacacaaagaatatatttcctggtgatgttaattggtttgtgcaacatgaatgggnaaaagaccaaggctggcactgccatgtactaattggaggaaaggactttagtcaagctcaagggaaatggtggagaaggcaactaaatgtttactggagcagatggttggtaacagcctgtaatgtgcaactaacaccagctgaaagaattaaactaagagaaatagcagaagacaatgagtgggttactctacttacttataagcataagcaaaccaaaaaagactataccaagtgtgttctttttggaaacatgattgcttactattttttaactaaaaagaaaataagcactagtccaccaagagacggaggctattttctttagcagtgactttggctggaaaactaactttttaaaagaaggcgagcgccatctagtgagcaaactatacactgatgacatgcggccagaaacggttgaaaccacagtaaccactgcgcaggaaactaagcgcggcagaattcaaactaaaaaagaagtttctattaaaactacacttaaagagctggtgcataaaagagtaacctcaccagaggactggatgatgatgcagccagacagttacattgaaatgatggctcaaccaggtggagaaaacctgctgaaaaatacgctagagatttgtacactaactctagccagaaccaaaacagcatttgacttaattttagaaaaagctgaaaccagcaaactaaccaacttttcactgcctgacacaagaacctgcagaatttttgcttttcatggctggaactatgttaaagtttgccatgctatttgctgtgttttaaacagacaaggaggcaaaagaaatactgttttatttcatggaccagccagcacaggcaaatctattattgcacaagccatagcacaagcagttggcaatgttggttgctataatgcagccaatgtaaactttccatttaatgactgtaccaacaagaacttgatttgggtagaagaagctggtaactttggacagcaagtaaaccagtttaaagccatttgctctggtcaaactattcgcattgatcaaaaaggaaaaggcagcaaanagattgaaccaacaccagtcatcatgaccacaaatgagaacattacagtggtcagaataggctgcgaagaaagaccagaacacactcaaccaatcagagacagaatgcttaacattcatctaacacataccttgcctggtgactttggtttggttgacaaaaatgaatggcccatgatttgtgcttggttggtaaagaatggttaccaatctaccatggcaagctactgtgctaaatggggcaaagttcctgattggtcagaaaactgggcggagccaaaggtgccaactcctataaatttactaggttcggcacgctcaccattcacgacaccgaaaagtacgcctctcagccagaactatgcactaactccacttgcatcggatctcgaggacctggctttagagccttggagcacaccaaatactcctgttgcgggcactgcagaaacccagaacactggggaagctggttccaaagcctgccaagatggtcaactgagcccaacttggtcagagatcgaggaggatttgagagcgtgcttcggtgcggaaccgttgaagaaagacttcagcgagccgctgaacttggactaaggtacgatggcgcctccagctaaaagagctaaaagaggtaagggtttaagggatggttggttggtggggtattaatgtttaattacctgttttacaggcctgaaatcacttggttttaggttgggtgcctcctggctacaagtacctgggaccagggaacagccttgaccaaggagaaccaaccaatccatctgacgccgctgccaaagagcacgacgaggcctatgatcaatacatcaaatctggaaaaaatccttacctgtacttctctgctgctgatcaacgctttattgaccaaaccaaggacgccaaagactggggaggcaaggttggtcactacttttttagaaccaagcgcgcttttgcacctaagcttgctactgactctgaacctggaacttctggtgtaagcagagctggtaaacgcactagaccacctgcttacatttttattaaccaagccagagctaanaanaaacttacttcttctgctgcacagcaaagcagtcaaaccatgagtgatggcaccagccaacctgacagcggaaacgctgtccantcagctgcaagagttgaacgagcagctgacgnccctggaggctctgggggtgggggctctggcgggggtggggttggtgtttctactgggtcttatgataatcaaacgcattatagattcttgggtgacggctgggtagaaattactgcactagcaactagactagtacatttaaacatgcctaaatcagaaaactattgcagaatcagagttcacaatacaacagacacatcagtcaaaggcaacatggcaaaagatgatgctcatgagcaaatttggacaccatggagcttggtggatgctaatgcttggggagtttggctccagccaagtgactggcaatacatttgcaacaccatgagccagcttaacttggtatcacttgatcaagaaatattcaatgtagtgctgaaaactgttacagagcaagacttaggaggtcaagctataaaaatatacaacaatgaccttacagcttgcatgatggttgcagtagactcaaacaacattttgccatacacacctgcagcaaactcaatggaaacacttggtttctacccctggaaaccaaccatagcatcaccatacaggtactatttttgcgttgacagagatctttcagtgacctacgaaaatcaagaaggcacagttgaacataatgtgatgggaacaccaaaaggaatgaattctcaattttttaccattgagaacacacaacaaatcacattgctcagaacaggggacgaatttgccacaggcacttactactttgacacaaatccagttaaactcacacacacgtggcaaaccaaccgtcaacttggacagcctccactgctgtcaacctttcctgaagctgacactgatgcaggtacacttactgctcaagggagcagacatggaacaacacaaatgggggttaactgggtgagtgaagcaatcagaaccagacctgctcaagtaggattttgtcaaccacaccatgactttgaagccagcagagctggaccatttgctgccncaaaagttccagcagatattactcaaggagtagacaaagaagccaatggcagtgttagatacagttatggcaaacagcatggtgaaaattgggcttcacatggaccagcaccagagcgctacacatgggatgaaacaagctttggttcaggtagagacaccaaagatggttttattcaatcagcaccactagttgttccaccaccactaaatggcattcttacaaatgcaaaccctattgggactaaaaatgacattcatttttcaaatgtttttaacagctatggtccactaactgcattttcacacccaagtcctgtataccctcaaggacaaatatgggacaaagaactagatcttgaacacaaacctagacttcacataactgctccatttgtttgtaaaaacaatgcacctggacaaatgttggttagattaggaccaaacctaactgaccaatatgatccaaacggagccacactttctagaattgttacatatggtacatttttctggaaaggaaaactaaccatgagagcaaaacttagagctaacaccacttggaacccagtgtaccaagtaagtgctgaagacaatggcaactcatacatgagtgtaactaaatggctaccaactgctactggaaacatgcagtctgtgccgcttataacaagacctgttgctagaaatacttactaactaaccatgctttttctttctgtacttcatatattattaagactaatanagatacaacatagaaatataatattacatatagatttaagaaatagaataatatggtacttagtaactgttaanaataatagaacctttggaataacaagatagttagttggttaatgttagatagaataagaagatcatgtataatgaataaaagggtggaagggtggttggtaggttaatgttagatagaataagaagatcatgtataatgaataaaagggtggaagggtggttggtaggtattcccttagacttgatgttaaggaccaaaaaaataataaaacttttttaaaactcaaccaagactactgtctattcagtgaaccaactgaaccattagtattactatgtttttagggtgggaggtcaatcaatcaggaa